## Slide 1: Proposal doc for MS11
Prepared By
Sevanand Singh

## Slide 2: Agenda
Dolby Technology(MS11 and MS10)
BBC CANVAS
Diff Between MS11 and MS10
Supported in STAUDLX
Modification Required for MS11
Modification Required for CANVAS

## Slide 3: Dolby Technology(MS10 and MS11)

## Slide 5
MS10 Stereo Audio Mixing

## Slide 6: Dolby Technology MS11

## Slide 11: BBC CANVAS

## Slide 12: BBC CANVAS Main program Stereo Input

## Slide 13: BBC CANVAS Main program Multichannel Input

## Slide 14: Input Stream Type
MPEG-1 Layer II
Dolby E-AC-3
Multi-channel HE-AAC
Stereo HE-AAC and LC-AAC
Receiver-mix audio description
MPEG-1 Layer III
Note: *Non-Program Sound may generate from any source (ALSA, Extrn MP3 decoder).
*Non-Program sound is assumed to be premixer to stereo PCM.

## Slide 15: Control on Audio description
Audio description disabled
Audio description mixed with all audio outputs
Audio description mixed with audio on SPDIF output
main programme sound sent to all other audio outputs without AD on PCMPlayers.

## Slide 16: Diff Between MS11 and MS10

## Slide 17: Diff Between MS11 and MS10
 | MS10 | MS11
Channel Supported | Stereo | MultiChannel
Sampling Freq | 32, 44.1 and 48 Transcoding supported only for 48KHz | 32, 44.1 and 48 Transcoding supported for all sampling freq's
No of Output | ByPass over HDMI, , Trancoded DD and Stereo PCM. | ByPass Over HDMI, Transcoded DD, Multichannel PCM and Stereo PCM
Transcoded Output | Transcoding will be applied at primary decoder(Before mixing) | Transcoding will be applied after mixing + DV
NOTE: DDRE tansform will produce stereo, multichannel
and Transcoded output.

## Slide 18: Supported in STAUDLX

## Slide 19: Generic audio driver chain for MS10
PCMP0
SPDIF0
PP2
PP0
PCMP1
PP1
CD1
CD0
SPDIFF0
DEC1
DEC0
MIX0
M
U
X
M
U
X
HDMI
Comp/PCM
P
I
T
SPDIF
Comp/PCM
Analog
PCM O/P
 | Compressed
 | Uncompressed
 | Comp/Uncomp Data
 | Temparary Connection
 | MetaData Flow

## Slide 20: Implementation of MS10 in staudlx driver
Basic config:
  Configure mixer in FIXED_OUTPUT_NO_SAMPLES 1 Means output no. of sample = input no. of sample.
MetaData Handling
  For DD+, metadata extracted from decoder/pes header/default.
  For Dolby Pulse, metadata extracted from PES header/default.
  DD+ metadata are extracted from DecoderOutputCmdParam_t framestatus.
  Carry these metadata to mixer module through Appdata_p field of memoryblock(for dd+) or through flag element of memoryblock.
  Mixing metadata are FADE and PAN.
    FADE means gain factor applied on primary input
    PAN means secondary mono audio angular position in 360*

## Slide 21: Implementation of MS10 in staudlx driver
Transcoded buffer:
  Transcoded Dolby digital buffer is extracted from main decoder.
  Transcoding is disabled for secondary decoder.
  Output no. sample of primary and secondary decoder is 1536(to make transcoding possible).
  DD+ to DD is handled by lx decoder. No encoder is required.
  Dolby pulse to DD is done by DDCO encoder at firmware side (encoder is tightly coupled with decoder). No saparete encoder module connected.

## Slide 22: Implementation of MS10 in staudlx driver
For DD+ stream, we supported multiple stream ID’s within single PID.
  In this case, we internally connect CD0 output to DEC1 in STAUD_IPSetADSubStreamID.
  Once user will select substream id 0 then internally we disconnect CD1 and reconfigure default connection.
  DD+ parser put I0 and In block in two separate block’s of different blockmanager’s.
For Dolby Pulse stream, parsing is done by lx.

## Slide 23: Modification Required for MS11

## Slide 24: At Parser Module
For DD+ over HDMI compatible:
  Should will not drop any data (unwanted independent substream or dependent substream or transcoded substream).
  Lx parser will take care of parsing correct data and drop redundent data.
  Proposed way:
  * Get both memory block (wait till both are not available).
  * Put required or unrequired frame into same memory block untill audio frame size of I0 will not become 1536 or consync will found.
  * Copy complete memory block in second block and put both of them.
  * No need to put substream ID info in block.

## Slide 25: At Parser Module
For Dolby Pulse over HDMI:
  ?
  We may take compressed frame aligned data for decoder(till now not supported by firmware).

## Slide 26: At decoder Module
Buffer handling for Stereo , Multichannel and Transcoded output.
* For Stereo output, staudlx driver may use Aux channel of 10 channel buffer.
Or
* Driver may provide addition buffer to handle stereo output
For dolby pulse, Driver may ask for frame aligned compressed output for HDMI.
  * Addition buffer require.
For DTS 2D, DTS encoder coefficients should be extracted in callback function and cascaded to appropriate module(Mixer/Postprocess).
Dolby Volume lite DV258

## Slide 27: At mixer Module
In MS10 implementation, mixer operate in o/p no. sample = i/p no. of sample.
For MS11/CANVAS, o/p no. of sample should be fixed(to align transcoded and PCM output) i.e. :
  For Dolby products 1536
  For DTS products 512
Mixing Metadata should be handled according to no.of sample send for processing.
For MS10, mixing metadata are frame aligned but for MS11 frame alignment may disturb(need to clarify with dolby).
Handling for Transcoded, Stereo and multichannel output.
Dolby volume lite.
While configuring DDRE config driver should inform whether data is Dolby volume processed or not.
DTS Encoder metadata processing

## Slide 28: At Post Process Module
- Buffer handling for stereo, multichannel and transcoded output.
Dolby Volume lite DV258
DTS Encoder metadata processing.

## Slide 29: Use Cases

## Slide 30: Single decode
PARSER
DECODER
DD+, DD and DP
DP HDMI Output
DD Transcoded o/p
Stereo PCM
MultiChannel PCM o/p
For DD+ and DD, Compressed unaltered i/p
should be taken from Parser module.
For Dolby pulse, Compressed frame aligned i/p
should be taken from decoder module.

## Slide 31: Dual Decode + Mixing
PARSER0
MIXER0
PARSER1
DEC1
DEC0
DD+, DD and DP
DD+, DD and DP
DP HDMI Output
DD Transcoded o/p
Stereo PCM
MultiChannel PCM o/p
Mixing Metadata
For DP, mixing metadata are extracted for PES Header
For DD+/DD/DTS, mixing metadata are extracted from decoder

## Slide 32: Thanks